## Slide 1
Click to add text

## Slide 2: Booting with TFTP and NFS
Software Engineering
RZ Team
Summary:
Install TFTP server.
Install NFS server.
Config Uboot to load data from server and connected via serial port.
Note: In this guideline, we going to use Ubuntu 16.04 as a host machine to setup environment.
My Tran

## Slide 3: Prerequisite
We need a Ubuntu machine to set up environment. In this case I recommend set up a virtual machine on Virtual box. If you have not installed a virtual machine yet. Please refer the link below to get tutorials:
https://www.wikihow.com/Install-Ubuntu-on-VirtualBox
Tera term to connect host machine and serial port
https://osdn.net/projects/ttssh2/releases/
Moba exterm to connect ssh and other session:
https://mobaxterm.mobatek.net/
Usb to serial driver

## Slide 4: Setup TFTP server
Download and install tftp-hpa by command:
sudo apt-get install tftpd-hpa
Note: /var/lib/tftpboot is used for TFTP server directory.

## Slide 5: Setup TFTP server
Check status of tftpd-hpa by command:
service tftpd-hpa status

## Slide 6: Setup TFTP server
Disable firewall by command:
sudo ufw disable

## Slide 7: Setup NFS server
Download and install NFS server by commands:
sudo apt-get install nfs-kernel-server

## Slide 8: Setup NFS server
Start a NFS server:
sudo /etc/init.d/nfs-kernel-server start

## Slide 9: Setup NFS server
Check status of nfs service:
service nfs-kernel-server status

## Slide 10: Setup NFS server
Create a directory for NFS:
sudo mkdir -p /nfs/rzg2m

## Slide 11: Setup NFS server
Open /etc/exports by text editor:
sudo vim /etc/exports
Add the following settings:
/nfs/rzg2m *(rw,no_subtree_check,sync,no_root_squash)

## Slide 12: Setup NFS server
Force an NFS server to read /etc/exports:
sudo exportfs –a
Confirm the NFS server starts successfully:
showmount -e localhost

## Slide 13: Prepare image, device tree and rootfs
Copy Image and device tree to /var/lib/tftpboot:
sudo cp <Image path> <device tree path> /var/lib/tftpboot

## Slide 14: Prepare image, device tree and rootfs
Copy rootfs to the mount point. In this case that is located at /nfs/rzg2m:
sudo cp <rootfs path> <mount_point>
Extract rootfs by command:
sudo tar –xvf <file_name>

## Slide 15: Set static ip for host machine
Network setting for virtual machine:
Select Device->Network->Network Settings

## Slide 16: Set static ip for host machine
Network setting:
Config setting following the picture

## Slide 17: Set static ip for host machine
Check network interfaces on host machine by command:
ifconfig

## Slide 18: Set static ip for host machine
In this case we set static ip for enp0s3, in other case that should be eth0. To set static ip for enp0s3 , edit setting in /etc/network/interfaces
Add setting below into the file:
iface enp0s3 inet static
address <IP>
netmask <netmask>

## Slide 19: Set static ip for host machine
Restart machine to apply new setting:
reboot
Setting static ip for enp0s3 by command:
sudo ifconfig enp0s3 <IP>

## Slide 20: Connect host machine and device
Connect serial port and Ethernet port to host machine
Serial
Power
Ethernet
Switch to power on

## Slide 21: Connect host machine and device
1.Connect PC and board via usb to serial device (CP210x)
2.Open tera term -> serial -> select port to connect

## Slide 22: Connect host machine and device
Select Setup -> serial port

## Slide 23: Connect host machine and device
Change Speed (baudrate) to 115200 and click new setting

## Slide 24: Connect host machine and device
Power on the board
Note: Before connecting the AC adapter to an electrical outlet, make sure that the switch for the power supply is turned off.

## Slide 25: Uboot config
Press any key to config Uboot

## Slide 26: Uboot config
Reset all environment variable by command
env default -a

## Slide 27: Uboot config
Set board ip and server ip by command
setenv ipaddr 192.168.1.5
setenv serverip 192.168.1.3
Set MAC address:
setenv ethaddr 74:90:50:00:00:d6
Setting bootcmd variable to specify name of Image and device tree file.
setenv bootcmd "tftp 0x48080000 Image; tftp 0x48000000 r8a774a1-hihope-rzg2n-ex-idk-1110wr.dtb; booti 0x48080000 - 0x48000000"
Setting bootars to specify the location of rootfs
setenv bootargs 'console=ttySC0,115200n8 ip=192.168.1.5:192.168.1.3::::eth0 rootwait root=/dev/nfs rw nfsroot=192.168.1.3:/nfs/rzg2n,nfsvers=3,tcp noinitrd nohlt panic=1 earlyprintk=ttySC0,115200n8'
Save environment if you want to autoboot with the config (optional)
saveenv

## Slide 28: Uboot config
Check connection by command:
ping ip_server
If you get this log, it all ok.

## Slide 29: Uboot config
Start booting by command:
boot
Check log on Terra term

## Slide 30: Uboot config
Login with user name ‘root’:

## Slide 31: Thank You For Your Attendance